Facades of houses
Types of facades in prefabricated buildings:

---
Plaster on boards
Plastering is currently the most popular way of finishing the outer walls of houses. The plaster surface must be strong and rigid, and the reinforcement must be embedded in the plaster, which will protect the facade from cracks.
It is best to use fiber cement boards for wall sheathing, which will also be a very good plaster undercoat. The joints between them are finished in the same way as joints between gypsum plasterboards, i.e. using fiberglass mesh tape and a special adhesive for leveling offered by the fiber cement manufacturer. Two layers of light plaster are laid on the prepared substrate, embedding a fiberglass mesh between them, which acts as a reinforcement. The last step is to apply a layer of decorative plaster, usually thin-layer.

---
Plaster on boards
Advantages:
- heavy boards with a layer of plaster improve the sound insulation of walls,
- the house looks like a stone house,
- the facade is an additional fire protection of the wall structure,
- plastered walls can be easily renewed by painting.
Disadvantages:
- laborious workmanship - it takes a lot of time to grout panels,
- between individual works - filling, laying the reinforced layer and plastering - one-day breaks are necessary.
- plastered walls are difficult to clean, especially if the plaster has a deep texture.

---
Facade plus insulation
The performance of plaster on a prefabricate houses can be combined with a seamless thermal insulation system called BSO. The basic components of this system are:
- adhesive for fixing thermal insulation boards,
- mortar for making the reinforced layer,
- fiberglass reinforcing mesh,
- mortar for thin-layer plaster - mineral, silicone, silicate or acrylic.

---
Facade plus insulation
Advantages:
- an additional layer of insulation increases the thermal insulation of the walls,
- an insulated house looks identical to a brick house,
- the facade is easy to renew by painting.
Disadvantages:
- making the facade is labor-intensive and easy to make errors,
- the facade is susceptible to mechanical damage - dents are formed after a strong impact on the wall,
- between individual works - carrying out the reinforced layer and plastering - one-day breaks are necessary,
- dirty facade is difficult to clean.

---
Siding - plastic facades
Siding - PVC panels, are intended for finishing frame houses. Due to the fact that their texture mimics the wood grain, they resemble painted facade boards. Their colors are very rich. Recently, there are also offered ones that look like clinker facades: they have the right color, texture and brick-shaped embossing.
Panels for sale are 3 to 6 m long, 23 to 29 cm wide and 1-2 mm thick. 1 m2 of such material weighs only 2 kg.
Siding is usually screwed horizontally to the elements of a wooden support grate attached to the rigid skeleton of the skeleton walls after covering them with windproofing foil. Installation is simple and you can do it yourself, especially since manufacturers offer a rich set of all auxiliary elements: corner strips, starting strips, window profiles, etc., which facilitate the finishing of various wall fragments.

---
Siding - plastic facades
Advantages:
- siding is very light and easy to cut, so it is easy and quick to mount,
- the facade is easy to clean - from time to time it is enough to wash it with water under pressure,
- the facade does not require any maintenance,
- it is resistant to moisture, temperature changes and frost.
Disadvantages:
- siding is not fire resistant: it is a flame retardant and flame retardant material, but in contact with fire and high temperature it is completely destroyed.

---
Wooden facade
Wooden facades look very attractive, so there is no shortage of supporters for such wall finish. For formwork, pine, spruce or larch boards from 1.8 to 3 cm thick, of different width and length are used. They usually have profiled inlets and outlets, making them easy to connect, but they are also used in other ways: for notches or for works.
The boards are nailed to a wooden load-bearing grid mounted on the OSB sheathing and bolted to the structural wall posts. Grate elements should be made of the same type of wood as boards. Boards are usually mounted horizontally. After installation, the surface is finished with varnish, varnish (so-called azure), decorative impregnation or paint.
Warning! The lower edge of the wooden facade should not be lower than 30 cm from the ground level - this will protect it from being splashed by rain drops bouncing off the ground. It is also important to leave a ventilation gap between the formwork and the wall surface, which will allow moisture to drain away from the inside of the building.

---
Wooden facade
Advantages:
- the formwork assembly is very fast, without any technological breaks.
Disadvantages:
- the correct execution of the facade requires professionalism,
- the facade must be protected against harmful weather conditions (rain, sun) and the development of fungi, mold and insects,
- every few years the facade needs renovation: it is usually necessary to sand it and re-paint or varnish,
- the facade is not fire resistant.

---
Brick wall
Such elevation is made of clinker, facing or silicate masonry bricks on the foundation. It is best if the house design provides a sufficiently wide foundation on which you can base an additional layer of bricks, because widening the foundation in the finished house is troublesome.
Bricks are built on incomplete joints: clinker - for special clinker mortar, and facing and silicate bricks - for traditional cement-lime mortar. After 3-4 days from the end of masonry, the joints are completed with a special jointing mass selected for the color of the bricks. The facade does not require plastering or painting. Silicate walls, however, should be covered with a special impregnation so that they do not get dirty.
Warning! A ventilation space 2-3 cm wide must be left between the wall and the rigid sheathing or an additional layer of insulation, which will allow the removal of condensation appearing between individual materials. There should be holes at the bottom and top of the facing that allow air to enter and evacuate.

---
Brick wall
Advantages:
- weatherproof facade, no maintenance required,
- due to the large mass of bricks, the soundproofing of the walls increases significantly,
- brick wall is very good protection against fire,
- the walls are resistant to accidental damage.
Disadvantages:
- a good facade requires a lot of professional knowledge,
- robots are time and work consuming.

---
Imitations of clinker and stone wall
A cheaper method to achieve a similar effect as a brick facade is to finish the skeleton house facade with ceramic or cement tiles. They are often used on parts of the facade. Such tiles are only a few millimeters thick, so you only need to glue them to a properly prepared substrate. Ceramic tiles can have different colors and textures, usually reminiscent of clinker bricks. Cement tiles imitate natural split stone.
The tiles are glued to a rigid sheathing, preferably from cement-fiber boards. They can replace plaster laid when insulating walls using a seamless thermal insulation system. Ceramic tiles require joint filling (grouting), but joints between cement tiles imitating stone are not filled.
Warning! Cement tiles should be coated with a mineral impregnation that will reduce their susceptibility to dirt.

---
Imitations of clinker and stone wall
Advantages:
- tiles are easy to lay,
- the facade is resistant to weather conditions,
- it is also resistant to damage, although less than a brick wall,
- protects the wooden structure from fire.
Disadvantages:
- making the facade is quite laborious and time consuming,
- requires accuracy during laying.

---
Large-size fiber cement boards
Large-size fiber cement boards are an interesting, though rarely used, facade material. They are made of cement mass (90%) mixed with synthetic fibers (10%). This creates a durable material that is not afraid of rapid temperature changes and is resistant to weather conditions. The panels have the dimensions: 120 × 305, 121.8 × 305, 121.8 × 244 or 120 × 260 cm. Their thickness can be from 3.2 to 18 mm. For construction, they are delivered in full or cut to size.
1 m2 of such facade weighs 10-18 kg, depending on the thickness of the panels. They are sold finished (painted with paint) or unfinished (primed only). The latter must be painted with facade paint or covered with thin-layer plaster. You can also buy slabs that are finished with stone aggregate.
Fiber cement panels are attached to a wooden or steel grid. Expansion joints must be left between individual panels: vertical widths of 6 mm and horizontal widths of 10 mm to allow the panels to deform under the influence of temperature changes, without which the facade could crack. Special aluminum profiles are laid in the gaps.

---
Large-size fiber cement boards
Advantages:
- the facade is durable and resistant to mechanical damage,
- it is done very quickly,
- no maintenance required,
- boards well protect the wooden structure against fire.
Disadvantages:
- the plates are quite difficult to clean,
- you need to renew them from time to time.