Types of house prefabrication

---
Types of house prefabrication
Open prefabrication
Closed prefabrication
Closed and full prefabrication

---
Open prefabrication is a system of building frame houses from prefabricated elements. In the prefabrication of open prefabrication, the external wall element is subject to a wooden wall structure covered with a wood-based panel. Roof construction may also be prefabricated.
In the open prefabrication system, after assembling the wall and roof structure together with the sheathing, other construction works are carried out already on the construction site:
• installation of thermal insulation,
• installation of vapor barrier film,
• installation of internal cladding panels,
• and installation of all kinds of installations.

---
Closed prefabrication
Closed prefabrication is a system for building FRAME HOUSES from elements as in open prefabrication, but the structure is filled with thermal insulation, and closed from the inside with an inner sheathing panel, usually a plasterboard or gypsum fiber board. The necessary installations are installed in the walls, which after assembling the house connects into the whole installation network. Houses built with a closed prefabrication system are called READY HOUSES. Installation of the house takes several days.

---
Closed and full prefabrication
https://www.youtube.com/watch?v=CAChT22yAek
Closed and complete prefabrication is the highest level of advancement in the closed prefabrication system. In this system, already in the factory, prefabricated window and door joinery with window sills are embedded and preliminary facade works are carried out.

---
Open prefabrication is a minimized prefabrication process limited to:
- assembly of the structure,
- installation of the outer sheathing,

---
Scheme of prefabrication open

---
In this condition, the elements are delivered to the construction site, where, after assembly, the remaining elements of the building are made:
- installation of windproofing foil,
- installation of thermal insulation,
- installation of the steam retarder foil,
- grate assembly - optional,
- installation of an additional layer of thermal insulation - optional,
- installation of inner sheathing,
- installation of window and door joinery,
- installation of external and internal window sills,
- electrical installation assembly,
- installation of additional thermal insulation,
- external cladding - plaster or wooden cladding.

---
A house constructed in this way is not subject to the definition of a finished house, because it takes about two to three months to complete the above scope of works, while ready houses should be erected within 2-3 days.